The Sound Professionals

High SPL Battery Filter Module

(SP-HPM-1)

Instructions

# Introduction

Congratulations on your purchase of The Sound Professionals High SPL battery/filter module. This power supply will enable you to achieve the best possible performance in high SPL situations from your Sound Professionals microphones.

The battery module is constructed of sturdy ABS plastic that will protect the internal components from mechanical damage. The output cable is terminated with a standard high quality, right angle 1/8” stereo phone plug.

The battery/filter module is a self-contained power and filter unit. To access the battery (included and already installed) for replacement, simply remove the 4 screws located in each corner of the battery/filter unit and remove the cover. The 9-volt battery can now be lifted out and replaced when necessary. The battery module uses a standard 9-volt battery that will last between 300 and 500 hours of continuous use. It is recommended that you change the battery at least once per year.

Preparing to make a recording

The first step in making a recording is to plug each microphone’s connector into one of the battery module’s input jacks. The jacks and connectors are keyed so that they only fit together one way. Push the microphone plug into the jack until you hear a ‘click’. The plug is now locked in place. To remove the plug, push the black button on the plug and pull the plug straight out.

Next, turn on the power supply by pulling the handle of the switch out and move it over to the side marked “-“ which indicates that the battery module is “on”. The handle of the switch will spring back into place. This switch has a locking feature to prevent accidental movement of the switch handle. The microphones are now receiving power from the battery module, and you are ready to proceed.

Before making your first important recording, it is suggested that you experiment with your new microphones and battery/filter unit a bit. By removing the 4 screws that hold the cover on the battery/filter module, you will access the red switch that selects the bass roll-off for each channel. You should experiment with the bass roll-off to see which setting (flat or rolled-off) produces the sound that you like the best.

It is usually desirable to have the left and right switch set to the same frequency; however, they can be set independently if desired.

Once you have decided upon a setting for the bass roll-off switches, close the battery/filter module. You do not need to reinstall the screws if you do not wish to do so. The lid of the module can be safely held on with a heavy rubber band if you wish, which will allow easier access to the interior of the module to make any adjustments necessary. Now you may plug the 1/8” stereo output cable into your recorder using one of the following procedures:

- If you are going to record very quiet sounds, (nature sounds, human speech, chamber music, meetings, etc.), it is suggested that you use the microphone “in” jack of your recorder using the -20dB setting (if you have one). This should produce excellent results with these types of sources. You may find it necessary to change to the different -dB setting if you have to turn the recording level controls up near their maximum settings at the -20dB setting.

- If you are going to be recording extremely loud sounds (rock concerts, full orchestras, close miked instruments, etc.), it is suggested that you use the “line in” jack of your recorder. This will produce excellent results with these types of sources.

You may now begin recording, following the directions provided by your recorder’s manufacturer. After a few minutes of recording, stop the recorder and listen to the recording you have just made. Adjust the microphone placement, recording levels and the bass roll-off switch as needed. Repeat this procedure until you are satisfied with the results. You are now ready to make that once-in-a-lifetime recording!

Remember to turn off the battery box when not in use to conserve battery power.

Care and Maintenance

Your Sound Professionals microphone system has been designed and manufactured to provide a lifetime of trouble-free service. When necessary, you may wipe the battery/filter module with a soft cloth moistened with clean water, removing excess moisture with a dry cloth.

Questions and help

If you have any questions regarding the use of your microphone system or require help with these instructions, please feel free to call us at 1-856-629-1619.

Warranty

The Sound Professionals will repair or replace, at our option, for a period of two years from the date of purchase, any Sound Professionals Binaural microphone system which in normal use has proven to be defective in workmanship or material, provided that the customer returns the product to us prepaid with proof of purchase. The Sound Professionals will not be responsible for any asserted defect which has resulted from normal wear, misuse, abuse or repair or alteration made or specifically authorized by anyone other than The Sound Professionals. Under no circumstances will The Sound Professionals be liable for incidental or consequential damages resulting from the use of this product. This warranty is The Sound Professionals sole warranty and sets forth the customer’s exclusive remedy, with respect to defective products; all other warranties, expressed or implied, whether of merchantability, fitness for purpose, or otherwise, are expressly disclaimed by The Sound Professionals.