### Manufactured by

# THE SOUND PROFESSIONALS

## SP-MICRO-1

www.soundprofessionals.com

The Sound Professionals

Micro microphones

(SP-MICRO-1)

Instructions

##### Introduction

Congratulations on your purchase of The Sound Professionals Micro microphones (SP-MICRO-1). These microphones represent the state of the art in ultra miniature condenser microphones. With reasonable care, these microphones will produce a lifetime of accurate recordings and listening enjoyment. These microphones can be used alone with any recorder or mixer supplying a bias voltage of 1.5 to 4 volts at its mic input. In addition, the SP-MICRO-1 can be used in conjunction with the optional extension cable (SP-SPSC-1).

The microphones themselves are housed in tough black rubber sleeves that protect the microphone capsules. The microphone capsules are wired together into a high quality gold plated stereo 1/8” phone jack.

##### Preparing to make a recording

Before making your first important recording, it is suggested that you experiment with your new microphones a bit.

Using the SP-MICRO-1 directly into the recorder:

First, verify that your recorder outputs the recommended voltage. (Damage to the microphones resulting from overpowering them is not covered under warranty). Once verified, if you are using the microphones alone, simply plug the SP-MICRO-1 into your recorder or mixer’s microphone input jack. If necessary, switch on the power source at the mic input (see the manufacturer’s instructions for more details on this). Once the microphone is receiving power from your recorder, you are ready to proceed. It is suggested that you use the -20dB setting (if available).

Using the SP-MICRO-1 in conjunction with the optional extension cable:

If you are using the SP-SPSC-1 extension cable, plug the microphones into the female jack of the extension cable and plug the male end of the extension cable into your recorder, using the same procedure as described above.

Using the SP-MICRO-1 in conjunction with the optional battery modules:

IMPORTANT: The SP-MICRO-1 is not designed to work with a battery module. DO NOT plug them into a battery module.

The next step is to determine microphone placement. The microphones, being very small, can be placed almost anywhere. For true binaural recordings, the best place to clip them is on either side of your (or an artificial) head, possibly on a pair of eyeglasses or a hat. With this placement, recordings are made with the microphones pointed out to the sides, not facing the performers…..similar to the way your ears point to the sides. This will produce exceptionally true and accurate Binaural recordings when played back using headphones. It is very important that the left/right placement is maintained throughout the recording and playback process; otherwise, the recording will sound like the performers were seated behind you instead of in front of you.

For standard stereo recordings that will be played back through loudspeakers, it is usually suggested that the microphones be attached to any solid object (even your shoulders will do) and placed about 18-24” apart from each other, facing forward. This will produce superb stereo recordings for playback through loudspeakers or headphones.

You may now begin recording, following the directions provided by your recorder’s manufacturer. After a few minutes of recording, stop the recorder and listen to the recording you have just made. Adjust the microphone placement and recording levels as needed. Repeat this procedure until you are satisfied with the results. You are now ready to make that once-in-a-lifetime recording!

##### Care and Maintenance

Your Sound Professionals Micro Binaural microphones have been designed and manufactured to provide a lifetime of trouble-free service. When necessary, you may wipe the cables with a soft cloth moistened with clean water, removing excess moisture with a dry cloth. The front of the microphone capsules should be protected from dust and dirt, and should not be moistened.

##### Questions and help

If you have any questions regarding the use of your microphone system or require help with these instructions, please feel free to call us at 1-856-629-1619.

#### Warranty

The Sound Professionals will repair or replace, at our option, for a period of one year from the date of purchase, any Sound Professionals Micro Binaural microphone system which in normal use has proven to be defective in workmanship or material, provided that the customer returns the product to us prepaid with proof of purchase. The Sound Professionals will not be responsible for any asserted defect which has resulted from normal wear, misuse, abuse or repair or alteration made or specifically authorized by anyone other than The Sound Professionals. Under no circumstances will The Sound Professionals be liable for incidental or consequential damages resulting from the use of this product. This warranty is The Sound Professionals sole warranty and sets forth the customer’s exclusive remedy, with respect to defective products; all other warranties, expressed or implied, whether of merchantability, fitness for purpose, or otherwise, are expressly disclaimed by The Sound Professionals.