### Manufactured by

# THE SOUND PROFESSIONALS

## SP-MICRO-2

www.soundprofessionals.com

The Sound Professionals

Micro microphones

(SP-MICRO-2)

Instructions

#### Introduction

Congratulations on your purchase of The Sound Professionals Micro microphone (SP-MICRO-2). This microphone represents the state of the art in ultra miniature condenser microphones. With reasonable care, this microphone will produce a lifetime of accurate recordings and listening enjoyment. The microphone can be used alone with any recorder or mixer supplying a bias voltage of 1.5 to 4 volts at its mic input. In addition, the SP-MICRO-2 can be used in conjunction with the optional extension cable (SP-SPSC-1).

The microphone element is housed in a tough black rubber sleeve that protects the microphone capsule. The microphone capsule is wired into a high quality gold plated stereo 1/8” phone jack.

#### Preparing to make a recording

Using the SP-MICRO-2 directly into the recorder:

First, verify that your recorder outputs the recommended voltage. (Damage to the microphone resulting from overpowering them is not covered under warranty). Once verified, if you are using the microphone alone, simply plug the SP-MICRO-2 into your recorder or mixer’s microphone input jack. If necessary, switch on the power source at the mic input (see the manufacturer’s instructions for more details on this). Once the microphone is receiving power from your recorder, you are ready to proceed. It is suggested that you use the -20dB setting (if available).

Using the SP-MICRO-2 in conjunction with the optional extension cable:

If you are using the SP-SPSC-1 extension cable, plug the microphone into the female jack of the extension cable and plug the male end of the extension cable into your recorder, using the same procedure as described above.

Using the SP-MICRO-2 in conjunction with the optional battery modules:

IMPORTANT: The SP-MICRO-2 is not designed to work with a battery module. DO NOT plug them into a battery module.

The next step is to determine microphone placement. The microphone, being very small, can be placed almost anywhere. You can use adhesive tape to hold it in place if you wish, or just push it through the buttonhole of a shirt.

You may now begin recording, following the directions provided by your recorder’s manufacturer. After a few minutes of recording, stop the recorder and listen to the recording you have just made. Adjust the microphone placement and recording levels as needed. Repeat this procedure until you are satisfied with the results.

#### Care and Maintenance

Your Sound Professionals Micro microphone has been designed and manufactured to provide a lifetime of trouble-free service. When necessary, you may wipe the cables with a soft cloth moistened with clean water, removing excess moisture with a dry cloth. The front of the microphone capsules should be protected from dust and dirt, and should not be moistened.

#### Questions and help

If you have any questions regarding the use of your microphone system or require help with these instructions, please feel free to call us at 1-800-213-3021

#### Warranty

The Sound Professionals will repair or replace, at our option, for a period of one year from the date of purchase, any Sound Professionals Micro Binaural microphone system which in normal use has proven to be defective in workmanship or material, provided that the customer returns the product to us prepaid with proof of purchase. The Sound Professionals will not be responsible for any asserted defect which has resulted from normal wear, misuse, abuse or repair or alteration made or specifically authorized by anyone other than The Sound Professionals. Under no circumstances will The Sound Professionals be liable for incidental or consequential damages resulting from the use of this product. This warranty is The Sound Professionals sole warranty and sets forth the customer’s exclusive remedy, with respect to defective products; all other warranties, expressed or implied, whether of merchantability, fitness for purpose, or otherwise, are expressly disclaimed by The Sound Professionals.