The Sound Professionals

Dual Channel Preamplified Microphone

(SP-PASM-3)

Instructions

## Introduction

Congratulations on your purchase of The Sound Professionals dual channel preamplified microphone (referred to as the PASM in this booklet).  This preamp/microphone combination can be used in situations where you need a microphone that outputs a line level signal. In addition, this unit has an external stereo microphone jack for use with other microphones. In this situation, the PASM will act as a standard stereo preamp. The ‘plug in power’ feature, present at the mic input, can be used to power any microphone that requires a 9 volt D.C. power source.

The PASM is constructed of sturdy fiberglass reinforced plastic that will protect the internal components from mechanical damage. The output cable is terminated with a standard high quality, right angle 1/8” stereo mini plug.

To install new batteries, remove the three coin cell batteries and install three new 3-volt batteries of the same type (CR2016) noting the proper polarity ( “+” up).

## Preparing to use the preamp

Selecting the proper gain range

Your new preamplifier has adjustable gain, in 3 ranges, and is controlled by a small toggle switch. The 9vdc “plug in power” feature is present in all gain ranges. The “0dB” gain range is used for loud recordings, when you don’t need any additional amplification. With this range, the audio signal is not amplified. The “29dB” gain range is used for most recording situations (moderately loud to fairly soft). The “50dB” gain range is used for extremely quiet recording situations.

For best results, use the lowest gain range that adequately drives the line input of your recorder to an acceptable level. Using a gain range that is too high will result in overloading of the preamplifier input, called “Brickwalling”. In general, you want to use the least amount of amplification necessary to obtain a line level signal to drive your recording device.

Using the PASM  with a line level input device

If you are using the PASM with a recording or other device that requires a line level signal at it’s input, the output cable from the PASM into your recorder or mixer’s LINE input. Turn the level control of the PASM all the way down (counter-clockwise) and turn the preamp ‘on’ by flipping the power switch on.

# Using the PASM in conjunction with other microphones

If you are using the PASM  with a microphone other than the built-in microphone, the procedure for its use is the same as noted above. Be sure the microphone is designed to use at least 9 volts DC and has a 1/8” stereo phone plug. Plug your microphone into the mic input jack on the PASM. Plug the output cable from the PASM into your recorder or mixer’s LINE input. Turn the level control of the PASM all the way down (counter-clockwise) and turn the preamp ‘on’ by flipping the power switch up.

Turn on your recorder or mixer and prepare it for recording. For a recorder, set the recording level by following this procedure:

- Set the recording level to the maximum setting in the ‘manual recording’ mode (some recorders are always in manual mode). The recording level should be at maximum for the best overall dynamic range and lowest signal to noise ratio.

- While monitoring a source signal, turn up the level control on the preamp (the knob that rotates) so that the recording level meters are set per the manufacturer’s instructions (usually as high as possible without hitting the very top of the scale “0dB”).

You may now begin recording, following the directions provided by your recorder or mixer’s manufacturer. After a few minutes of recording, stop the recorder and listen to the recording you have just made. Adjust the microphone placement and recording levels as needed. Repeat this procedure until you are satisfied with the results. You are now ready to make that once-in-a-lifetime recording!

Remember to turn off the preamp when not in use to conserve battery power.

## Care and Maintenance

Your Sound Professionals  preamplifier has been designed and manufactured to provide a lifetime of trouble-free service. When necessary, you may wipe the exterior of the case with a soft cloth moistened with clean water, removing excess moisture with a dry cloth.

Questions and help

If you have any questions regarding the use of your preamplifier or require help with these instructions, please feel free to call us at 1-800-213-3021.

Warranty

The Sound Professionals will repair or replace, at our option, for a period of two years from the date of purchase, any Sound Professionals preamp which in normal use has proven to be defective in workmanship or material, provided that the customer returns the product to us prepaid with proof of purchase. The Sound Professionals will not be responsible for any asserted defect which has resulted from normal wear, misuse, abuse or repair or alteration made or specifically authorized by anyone other than The Sound Professionals. Under no circumstances will The Sound Professionals be liable for incidental or consequential damages resulting from the use of this product. This warranty is The Sound Professionals sole warranty and sets forth the customer’s exclusive remedy, with respect to defective products; all other warranties, expressed or implied, whether of merchantability, fitness for purpose, or otherwise, are expressly disclaimed by The Sound Professionals.