### Manufactured by

# THE SOUND PROFESSIONALS

## (SP-SPSM-4 thru 10)

www.soundprofessionals.com

The Sound Professionals

Single Point Stereo Gooseneck Microphone

(SP-SPSM-4 thru SP-SPSM-10)

Instructions

Introduction

Congratulations on your purchase of The Sound Professionals single point stereo gooseneck microphone. This microphone represents the state of the art in miniature condenser microphones. With reasonable care, this microphone will produce a lifetime of accurate recordings and listening enjoyment. This microphone can be used alone with any recorder supplying a bias voltage of 1.5 to 10 volts at its mic input, sometimes called “plug in power”. In addition, the mic can be used in conjunction with the optional extension cable (SP-SPSC-1), the removable mic stand mount (SP-DTS-5) or any of our optional battery modules for even greater flexibility and sound quality.

The microphone capsules are mounted on rugged, flexible arms that allow positioning of the mics for best performance. The flexible arms are connected to a standard, gold plated 1/8” stereo phone plug.

Included with the microphone and covering the front of each capsule is a removable black windscreen. For indoor recordings, the windscreens may be left off if desired. For outdoor recordings, or recordings of speech at close distances, it is recommended that they be installed.

Preparing to make a recording

Before making your first important recording, it is suggested that you experiment with your new microphones a bit.

#### Using the microphone directly into the recorder

If you are using the microphone alone, simply plug the microphone into your recorder or mixer’s microphone input jack supplying 1.5 to 10 volts D.C. bias power. If you are resting the recorder on a table or other surface, we suggest that you bend the arms of the microphone down so that they rest on the same surface as your recorder, thereby taking the weight of the microphone off of the mic input jack and placing it on the arms of the microphone.

Using the microphone in conjunction with the optional extension cable

If you are using the SP-SPSC-1 extension cable, plug the microphone into the female jack of the extension cable and plug the male end of the extension cable into your recorder, using the same procedure as described above.

Using the microphone in conjunction with the optional microphone mount

If you are using the SP-DTS-5 microphone mount, loosen the screw in the mount and push the microphone into the hole in the microphone mount. Tighten the screw in the mount to hold the mic in place. Make sure the microphone is pushed into the mount far enough that you will be able to plug in the extension cable.

Using the microphone in conjunction with the optional battery modules:

If you are using the microphones and/or the extension cable with any of the battery/filter modules, plug the microphone (or the male end of the extension cable if you are using it) into the input jack of the battery module. The microphone is now receiving power from the battery module (refer to the battery/filter module’s instructions for additional information regarding it’s use). Since the microphone will receive power anytime it is connected to the battery/filter module, be sure to disconnect it from the module when not in use.

In most cases, when using the battery module, and you are going to be recording relatively loud sounds (rock concerts, full orchestras, close miked instruments, etc.), it is suggested that you use the “line in” jack of your recorder or mixer. This will produce excellent results with these types of sources.

If you are going to record very quiet sounds, (nature sounds, human speech, chamber music, meetings, etc.), it is suggested that you use the microphone “in” jack of your recorder using the -20dB setting. This should produce excellent results with these types of sources. You may find it necessary to change to a different -dB setting if you have to turn the recording level controls up near their maximum settings at the -20dB setting.

Once you have plugged the output cable from the battery module into your recorder or mixer, you are ready to proceed.

You may now begin recording, following the directions provided by your recorder or mixer’s manufacturer. After a few minutes of recording, stop the recorder and listen to the recording you have just made. Adjust the microphone and recording levels as needed. Repeat this procedure until you are satisfied with the results. You are now ready to make that once-in-a-lifetime recording!

Care and Maintenance

Your Sound Professionals  microphone has been designed and manufactured to provide a lifetime of trouble-free service. When necessary, you may wipe the exterior of the microphone with a soft cloth moistened with clean water, removing excess moisture with a dry cloth.

The miniature microphone should not be moistened. Always keep the windscreens in place on the front of the microphone capsules when not in use.

Questions and help

If you have any questions regarding the use of your microphone or require help with these instructions, please feel free to call us at 1-800-213-3021.

Warranty

The Sound Professionals will repair or replace, at our option, for a period of one year from date of purchase, this Sound Professionals microphone that in normal use has proven to be defective in workmanship or material, provided that the customer returns the product to us prepaid with proof of purchase. The Sound Professionals will not be responsible for any asserted defect which has resulted from normal wear, misuse, abuse or repair or alteration made or specifically authorized by anyone other than The Sound Professionals. Under no circumstances will The Sound Professionals be liable for incidental or consequential damages resulting from the use of this product. This warranty is The Sound Professionals sole warranty and sets forth the customer’s exclusive remedy, with respect to defective products; all other warranties, expressed or implied, whether of merchantability, fitness for purpose, or otherwise, are expressly disclaimed by The Sound Professionals.