Manufactured by

# THE SOUND PROFESSIONALS

## SP-HBA-2

www.soundprofessionals.com

The Sound Professionals

"Laff's Headbanger"

Premium Headphone Amplifier

### Instructions

Introduction

Congratulations on your purchase of "Laff's Headbanger" headphone amplifier. This headphone amplifier represents the state of the art in miniature headphone amplifiers. With reasonable care, this amplifier will produce many years of listening enjoyment.

This amplifier features a small, lightweight, impact resistant black plastic case with an easy-to-access 9-volt battery compartment. The signal from the player/recorder is fed to the amplifier via a flexible shielded cable terminated in high quality right angle 1/8" stereo mini plug.

Using the “Headbanger”

To use the "Headbanger", first remove the battery compartment door by sliding it toward the bottom of the amplifier. Connect a standard size 9 volt battery (alkaline or rechargeable types are recommended) to the battery clip. Insert the battery into the battery compartment. Reinstall the battery compartment door by sliding it back into place.

Now, connect one end of the stereo patch cable into your player/recorder’s headphone (or line out) jack. Plug your headphones into the Headbanger’s “out” jack and turn the Headbanger on by flipping the switch to the “on” position. When not in use be sure to move the switch to the “off” position to extend battery life.

Turn the volume of your player/recorder and the output level control on the Headbanger all the way down. This is very important, as the Headbanger is capable of very high sound pressure levels. Start your player/recorder.

- If you are using the headphone output of your player/recorder, turn up the volume on the player/recorder near its maximum undistorted level. Slowly turn up the Headbanger’s level control to reach the desired volume level.

- If you are using your player/recorder’s line output, no adjustment on your player/recorder is necessary. Slowly turn up the Headbanger’s level control to reach the desired volume level.

That’s it! You can now enjoy listening to your favorite player/recorder with any commercially available headphones and the “Headbanger” will produce all the power necessary to properly drive them.

Specifications

| Weight | 4 ounces (including battery) |
| --- | --- |
| Distortion | 0.1% at full output |
| Frequency Response | 5Hz to >110kHz (-1dB) |
| Max. Output level | 1.7Vrms |
| Noise | less than portable players (very low) |
| Output Power | 375mW into 8-ohms |
| Input Impedance | 33Kohms, minimum |
| Running Time | Approximately 26 hours with 9 volt Alkaline battery, depending on audio level |
| Controls | On/Off switch |
| Output | 1/8" mini stereo jack |
| Input | Shielded cable with 1/8" mini stereo plug |

Disclaimer

Protecting your hearing is your responsibility. The Sound Professionals and Stephen H. Lafferty are not responsible for any misuse of this device or hearing damage that you or anyone who uses this device may incur. Do not use at loud sound pressure levels. Never listen at any sound pressure level that leaves your ears ringing or leave your hearing temporarily depressed or impaired. Any damage or loss of hearing or any other physical or mental condition caused by the use or misuse of this product is the responsibility of the user alone.

Questions and help

If you have any questions regarding the use of your “Headbanger” or require help with these instructions, please feel free to call us at 1-800-213-3021.

Warranty

The manufacturer will repair or replace, at their option, for a period of 2 years from the date of purchase, any headphone amplifier, which in normal use has proven to be defective in workmanship or material, provided that the customer returns the product to us prepaid with proof of purchase. The Sound Professionals  and/or the manufacturer will not be responsible for any asserted defect which has resulted from normal wear, misuse, abuse or repair or alteration made or specifically authorized by anyone other than The Sound Professionals or the manufacturer. Under no circumstances will The Sound Professionals or the manufacturer be liable for incidental or consequential damages resulting from the use of this product. This warranty is the sole warranty and sets forth the customer’s exclusive remedy, with respect to defective products; all other warranties, expressed or implied, whether of merchantability, fitness for purpose, or otherwise, are expressly disclaimed by the manufacturer and The Sound Professionals.