### Manufactured by

# THE SOUND PROFESSIONALS

www.soundprofessionals.com

The Sound Professionals

Mini Portable PA System

Instructions

# Instructions

##### Introduction

Congratulations on your purchase of The Sound Professionals mini PA system. This product has been built to provide years of trouble free service. If you have any questions regarding the use of your system, please feel free to call 800-213-3021 for assistance.

Preparing for first use

After removing the contents from the box, verify that you have all of the components that you ordered.

Along with this manual, there is a manual provided for the wireless system that has been installed in your PA system. Please read this manual to become familiar with the wireless components of your system. Note that the built-in microphone on the transmitter referred to in this manual has been replaced with a universal female 3.5mm jack to allow you to connect the various microphones that are part of this system to the transmitter. The smaller jack that is built into the transmitter is the 2.5mm jack and is intended only for the standard lapel microphone that is included in your system. There is also a manual for the amplifier portion of the system. Please read this manual to familiar with the amplifier component of the system.

To get ready to use your system for the first time, first decide which microphone (if you bought more than one) you want to try first. If you have no already done so, install a AAA battery in the transmitter and turn the power switch to ‘on’. The mute switch, which allows you to temporarily stop sound from coming out of the system, should be off.

If you are going to use the optional neck microphone:

Unroll the flexible gooseneck and plug the 3.5mm male connector into the 3.5mm female jack on the transmitter. You may have to push hard to get the connector to seat all the way down – this is normal. (You may want to remove the clip on the back of the transmitter if you plan on using this microphone most of the time. This will allow the transmitter to lay flat against your body. Save the clip for future use with the lapel style microphones). Place the gooseneck around your neck so that the microphone is one side of your body and the transmitter on the other. Bend the microphone end up toward your mouth so that it is a few inches away from your mouth.

If you are going to use one of the optional  plug-in microphones:

Plug the microphone into the 3.5mm female jack on the transmitter. You may have to push hard to get the connector to seat all the way down – this is normal.

If you are going to use the standard lapel clip-on microphone:

Plug the microphone into the 2.5mm female jack on the transmitter. Clip the microphone onto a lapel of collar. Refer to the wireless instruction manual for further details.

Turn all controls on the amplifier to minimum (to the left). Push the power switch down to turn on the amplifier. Slowly turn up the volume control on the amplifier to get the desired sound level from the speaker. If you hear feedback (a howling sound), turn down the amplifier a bit, or move away from the amplifier. Having the speaker facing away from you (or in front of you, facing away) also helps. The closer the mic is to you mouth, the less feedback you will get. If you wish, you can adjust the ‘voice’ control on the amplifier to change the tone. The gain and overdrive controls are not used for voice amplification, but can be used if you wish to plug a musical instrument into the amplifier. Doing so will mix the sound from the instrument and the microphone if both are used at the same time.

Questions and help

If you have any questions regarding the use of your PA system or require help with these instructions, please feel free to call us at 1-800-213-3021.

Warranty

The Sound Professionals will repair or replace, at our option, for a period of two years from the date of purchase, any Sound Professionals microphone component, which in normal use has proven to be defective in workmanship or material, provided that the customer returns the product to us prepaid with proof of purchase. The amplifier and wireless components are covered under the warranty provided by their respective manufacturer. The Sound Professionals will not be responsible for any asserted defect, which has resulted from normal wear, misuse, abuse or repair or alteration, made or specifically authorized by anyone other than The Sound Professionals. Under no circumstances will The Sound Professionals be liable for incidental or consequential damages resulting from the use of this product. This warranty is The Sound Professionals sole warranty and sets forth the customer’s exclusive remedy, with respect to defective products; all other warranties, expressed or implied, whether of merchantability, fitness for purpose, or otherwise, are expressly disclaimed by The Sound Professionals.