The Sound Professionals

Dual Channel Microphone Preamp

(SP-PREAMP-2)

Instructions

## Introduction

Congratulations on your purchase of The Sound Professionals dual channel microphone preamplifier SP-PREAMP-2.  This preamp can be used in situations where the signal coming from your microphones need to be strengthened before they are plugged into your recorder or mixer. The ‘plug in power’ feature, built into this preamplifier, can be used to power any microphone that requires a 9 volt D.C. power source.

The preamp is encased in tough rubber that will protect the internal components from mechanical damage. The output cable is terminated with a standard high quality, right angle 1/8” stereo mini plug.  The input is a 1/8” stereo mini plug.

To access the battery compartment, slide the elastic cover aside on the top of the unit. Using a small screwdriver or similar tool, lift and slide the two button cell batteries out of the battery holder. Install three new 3-volt batteries of the same type (CR2016) noting the proper polarity ( “+” up) and move the elastic back over the battery compartment.

If you wish, you can apply the Velcro strip to your recording device so that the preamp will mount securely. To do this, remove the tape from the back of the Velcro strip and apply it to your recording device. Press down firmly.

## Preparing to use the preamp

Selecting the proper gain range

Your new preamplifier has adjustable gain, in 3 ranges, and is controlled by a small toggle switch. The 9vdc “plug in power” feature is present in all gain ranges. The “0dB” gain range is used for loud recordings, when you don’t need any additional amplification. With this range, the audio signal is not amplified. The “29dB” gain range is used for most recording situations (moderately loud to fairly soft). The “50dB” gain range is used for extremely quiet recording situations.

For best results, use the lowest gain range that adequately drives the line input of your recorder to an acceptable level. Using a gain range that is too high will result in overloading of the preamplifier input, called “Brickwalling”. In general, you want to use the least amount of amplification necessary to obtain a line level signal to drive your recording device.

Using the SP-PREAMP-2 with any Sound Professionals  microphone

If you are using the SP-PREAMP-2  with one of our microphones, simply plug the microphone’s connector into the preamp input jack. Switch the preamp “on” by moving the switch over to the side toward the “-“ indicator. The microphone is now receiving power, the preamp is on and you are ready to proceed.

# Using the SP-PREAMP-2 in conjunction with other microphones

If you are using the SP-PREAMP-2  with a microphone other than a Sound Professionals microphone, the procedure is the same as noted above. Be sure the microphone is designed to use at least 6 volts DC and has a 1/8” stereo phone plug.

Plug the 1/8” stereo output cable from the preamp into your recorder or mixer’s LINE input.

Turn on your recorder or mixer and prepare it for recording. Set the recorder to ‘manual recording’ (some recorders are always in manual mode).

You may now begin recording, following the directions provided by your recorder or mixer’s manufacturer. After a few minutes of recording, stop the recorder and listen to the recording you have just made. Adjust the microphone placement and recording levels as needed. Repeat this procedure until you are satisfied with the results. You are now ready to make that once-in-a-lifetime recording!

Remember to turn off the preamp when not in use to conserve battery power. A fresh set of batteries will last about 20 hours.

## Care and Maintenance

Your Sound Professionals  preamplifier has been designed and manufactured to provide a lifetime of trouble-free service. When necessary, you may wipe the exterior of the case with a soft cloth moistened with clean water, removing excess moisture with a dry cloth.

## Questions and help

If you have any questions regarding the use of your preamplifier or require help with these instructions, please feel free to call us at 1-800-213-3021.

## Warranty

The Sound Professionals will repair or replace, at our option, for a period of two years from the date of purchase, any Sound Professionals preamp which in normal use has proven to be defective in workmanship or material, provided that the customer returns the product to us prepaid with proof of purchase. The Sound Professionals will not be responsible for any asserted defect which has resulted from normal wear, misuse, abuse or repair or alteration made or specifically authorized by anyone other than The Sound Professionals. Under no circumstances will The Sound Professionals be liable for incidental or consequential damages resulting from the use of this product. This warranty is The Sound Professionals sole warranty and sets forth the customer’s exclusive remedy, with respect to defective products; all other warranties, expressed or implied, whether of merchantability, fitness for purpose, or otherwise, are expressly disclaimed by The Sound Professionals.